J5
J2
J1
J4
J3
RC0
RC1
RC2
RD0
RD1
RD2
RD3
RE2
RA0
RA1
RA2
RA3
RA4
RA5
RE0
RE1
RD7
RD6
RD5
RD4
RC7
RC6
RC5
RC4
RB7
RB6
RB5
RB4
RB3
RB2
RB1
RB0
VIN
GND
GND
5V
3.3V
RESET
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
21
22
23
24
25
26
27
28
29
30
31

---
I²C connector with
master/slave selection
Serial source CTS enabled selection
Power sources selection
ICSP connector
Serial
Connector with Reset-via-RTS selection
Fuse protection
USB
Connector
Microchip PIC 18F4550 microcontroller
3.3V regulation
20MHz crystal (48MHz clocking with PLL)
5V regulation with diodes protection
Reset
Button
Shield connectors

---
Using AC/DC adapter, connected
to the jack, as power source
Also power the serial module
Using power coming from
USB connector
Also power the serial module
Using power coming from
the serial module
Invalid combination !
 Don't do this !
jack
USB
Serial
JP1
JP2
JP3
Serial source
JP4
jack
USB
Serial
JP1
JP2
JP3
Serial source
JP4
jack
USB
Serial
JP1
JP2
JP3
Serial source
JP4
jack
USB
Serial
JP1
JP2
JP3
Serial source
JP4
jack
USB
Serial
JP1
JP2
JP3
Serial source
JP4
jack
USB
Serial
JP1
JP2
JP3
Serial source
JP4

---
Reset-via-RTS enabled
RTS line enabled
(connected to pin RD4)
No RTS setup
RST
J7
RST
J7
RST
J7

---
CTS line enabled
(connected to pin RD5)
No CTS setup
CTS
JP7
CTS
JP7

---
JP5
JP6
I²C master enabled
Master/slave
JP5
JP6
I²C slave enabled (use this setup
if you don't care about I²C)
Master/slave